## Slide 1: The Van der Meer formula for rock slope stability at shallow water
Jentsje van der Meer – VdMC; IHE Delft
Thomas Lykke Andersen – Aalborg University
Mads Røge Eldrup – Aalborg University

## Slide 2: Contents
Recent developments and comparisons on rock stability formulae
Dataset of Van Gent et al. on shallow water
Stability analysis depending on relative water depth
Conclusions

## Slide 3
For plunging waves:
Hs/ΔDn50 = 6.2 P0.18 (Sd/N0.5)0.2 ξm-0.5
and for surging waves:
Hs/ΔDn50 = 1.0 P-0.13 (Sd/N0.5)0.2 cotα0.5 ξmP
Van der Meer formula (1988)
ξm < ξmc: plunging
ξm ≥ ξmc: surging
ξmc = {(6.2 / 1.0) * P0.31 √tanα}1/(P+0.5)
With the mean period Tm.
We now would like the spectral period Tm-1,0

## Slide 4
For plunging waves:
Hs/ΔDn50 = cpl 6.49 P0.18 (Sd/N0.5)0.2 ξm-1,0-0.5
and for surging waves:
Hs/ΔDn50 = csu 0.97 P-0.13 (Sd/N0.5)0.2 cotα0.5 ξm-1,0P
Van der Meer formula revisited (2021) – JCHS
ξm-1,0 < ξm-1,0c: plunging
ξm-1,0 ≥ ξm-1,0c: surging
ξm-1,0c = {(6.49 cpl / 0.97 csu ) * P0.31 √tanα}1/(P+0.5)
cpl = csu = 1 for original formula
cpl or csu < 1: less stable
cpl or csu > 1: more stable
Rewritten, not refitted
Rock Manual (2007): Applicable for deep water
h/Hm0d > 3

## Slide 5
For plunging waves:
Hs/ΔDn50 = 8.4 P0.18 (Sd/N0.5)0.2 (Hs/H2%) ξm-1,0-0.5 Rock Manual 5.139
and for surging waves:
Hs/ΔDn50 = 1.3 P-0.13 (Sd/N0.5)0.2 (Hs/H2%) cotα0.5 ξm-1,0P Rock Manual 5.140
Modified Van der Meer formula for shallow water by Van Gent (2003)
ξm-1,0 < ξm-1,0c: plunging
ξm-1,0 ≥ ξm-1,0c: surging
ξm-1,0c = {(8.4 / 1.3) * P0.31 √tanα}1/(P+0.5)
Deep water: H2%/Hs=1.4
cpl = 0.92 (8% lower)
csu = 0.96 (4% lower)
Rock Manual (2007): Applicable for shallow water
h/Hm0d < 3

## Slide 6: Working area Van der Meer formula
plunging, breaking waves
surging, non-breaking waves
Modified for shallow water: 8% and 4% lower

## Slide 7: Data set Van Gent et al.
Papers: Smith et al. (2002), Van Gent et al. (2003), Van Gent (2004)
Dataset, released a few years ago:
205 tests with single and double peaked spectra
https://www.researchgate.net/publication/320559323_Data-Stability_of_rock_slopes_with_shallow_foreshores

## Slide 8: Analysis of dataset on waves over the foreshore
Data division:
  h/Hm0d > 3: deep(er) water
  1.5 < h/Hm0d < 3: shoaling and some breaking
  1 < h/Hm0d < 1.5: shallow water, continuous wave breaking, linear decrease of Hs
  h/Hm0d < 1.0: very shallow water, heavy breaking, infragravity waves
The 1:30 slope does not show any shoaling for H1/3, where it should.
H2% cannot be predicted in a reliable way:
  use H1/3 toe or Hm0 toe
Hypothesis: VdM-formula is valid for h/Hm0d > 1.5

## Slide 9: H2% as design wave height
H2% cannot be predicted in a reliable way for h/Hm0d<1.5

## Slide 10: Expected behaviour at shallow water
?
Design wind waves,
sm-10>0.02
?
?
?
h/Hm0 d < 1.5

## Slide 11: Stability analysis: permeable core; cotα=4

## Slide 12: Stability analysis: permeable core; cotα=2

## Slide 13: Stability analysis: impermeable core; cotα=4

## Slide 14: Stability analysis: impermeable core; cotα=2

## Slide 15: Conclusions
The (rewritten) VdM-formula as well as the Modified formula do not work over the full area of shallow water;
For shallow water the (rewritten) VdM-formula is applicable at least up to h/Hm0d > 1.5;
More precise:
  the plunging wave equation is always applicable, down to surging waves;
  the surging wave equation is not applicable;
  in that region: horizontal lines with large unexplained scatter?
The prediction of H2% for design is unreliable for h/Hm0d<1.5;

## Slide 16: Thank you for your attention
Deltares is acknowledged for releasing the dataset